## Slide 1: CS 33 Discussion 1
April 7,2017

## Slide 2: Discussion 1C
TA: Aanchal Dalmia
Email: aanchal204@cs.ucla.edu
Office Hours: Wednesday11:30am-1:30pm
TA Room: BH 2432

## Slide 3: Agenda
Overview
How to access SEASNET Linux servers
Representing information as bits
Integers
  Representation : signed, unsigned
  Conversion, casting
  Expanding, truncating
  Addition, subtraction, multiplication, shifting
  Summary

## Slide 4: Overview of Course
http://web.cs.ucla.edu/classes/spring17/cs33/
Grading
  40% labs (4, each 10%)
  5% homework (5, each 1%)
  25% midterms (2, each 12.5%)
  30% final exam
Use Piazza for doubts
Discussion slides will be mailed

## Slide 5: Course Textbook
The course textbook:
– Computer Systems: A Programmer's Perspective 3rd Edition
– CAUTION: The 2nd Edition, 2nd International Edition and the 3rd Edition all have essentially the same homework questions... except the numbers are different.

## Slide 6: Getting Started
Class is based on C
It is highly recommended to work in a Linux environment, specifically the SEASnet Linux Servers
Assignments will be tested on SEASnet Linux servers

## Slide 7: Setup
To login to SEASnet you need to be connected to wireless network on campus
OR
Login with VPN Software
https://www.it.ucla.edu/bol/services/virtual-private-network-vpn-clients

## Slide 8: Setup Guide for Windows
Download PuTTY
https://the.earth.li/~sgtatham/putty/latest/x86/putty.exe

## Slide 9: PuTTY
First Run
Type lnxsrv@seas.ucla.edu for Host Name
Type SEASnet for Saved Sessions
Click Save
Click Open
Type your SEASnet username and password
Double-click SEASnet under Saved Sessions in the future

## Slide 10: Setup Guide for Mac

## Slide 11: Terminal
Type ssh <SEASnet username>@lnxsrv.seas.ucla.edu
Enter your password

## Slide 12: Copying from local machine to SEASnet
For Windows users:
– WinSCP: An scp client
– scp stands for secure copy. You use it to secure copy. https://winscp.net/eng/download.php
For Mac and Linux:
– scp is a command that can be issued directly. Open a terminal (for Mac: Applications -> Utilities ->Terminal)

## Slide 13: Copying from local machine to SEASnet
For Windows users:
– In “host name”, enter [username]@lnxsrv.seas.ucla.edu
– Right click a file and select upload or download.
For Mac and Linux:
– Local to remote:
scp [file name] [username]@lnxsrv.seas.ucla.edu:.
– Remote to local:
scp [username]@lnxsrv.seas.ucla.edu:<path to file> .

## Slide 14: Useful Linux Commands
● Linux command format:
● [command name] -X -Y -Z [argument]
● (X, Y, and Z are optional flags)
● Flags modify/specify the behavior of the command

## Slide 15: Useful Linux Commands
● pwd – print working directory
● ls – list contents of current directory
– ls -l (“-l” flag will print contents in long form)
● cd – change directory
– cd a (navigates to the “a” directory which is located in the current directory)
– cd .. (navigate to the parent directory)
– cd ../dir (navigate to a directory called “dir” that is located within the parent)
– cd . (navigate to the current directory. Great work)

## Slide 16: Useful Linux Commands
● Editing files. If you're interested familiarizing yourselves with Linux (which will have to happen eventually), it is recommended that you use “vi” or “emacs”.
– vi text.txt
– emacs text.txt
● Commands that start with a colon :
:w save
:x save and quit
:q quit (will trigger error if file hasn't been saved)
:q! quit without saving

## Slide 17: Useful Linux Commands
● The standard Linux C compiler is gcc.
– gcc main.c (compile the file main.c into an executable file with default name “a.out”)
– gcc main.c -o main (compile the file main.c into an executable file called “main”)
– gcc main.c -O2 (compile the file with optimizations, level 2)
● Executing executables
– ./main (executes the executable file called “main”)

## Slide 18: C (as opposed to C++)
● In a (very simplified) nutshell, C++ is an extension to C.
● The syntax of the language is nearly identical, but you will find that C lacks certain features, namely the “Object Oriented” paradigm.
● Some features are analogous, but have different names.

## Slide 19: C (as opposed to C++)
● In C++:
– for(int i = 0; i < size; i++)
● By default, gcc uses a 1990's C standard which prohibits declarations in “for” loops. As a result, you will have to do either
– int i;
– for(i = 0; I < size; i++)
● Or explicitly use gcc to compile with a different C standard
– gcc -std=c99 temp.c

## Slide 20: C (as opposed to C++)
Dynamic memory allocation
In C++:
– char * c_arr = new char[10];
– delete c_arr;
– “new” allows you to specify repetitions of a specific data type.

## Slide 21: C (as opposed to C++)
● In C, these declarations force you to be more specific. Instead of “new”, use “malloc” and instead of “delete”, use “free”.
– char * c_arr = (char *) malloc(sizeof(char) * 10);
– free(c_arr);
● Note: These are analogous but not the same.
● “malloc” and other “_alloc” variations operate on the principle that you're specifying a specific amount of memory to allocate rather than a specific data type.

## Slide 22: C (as opposed to C++)
Instead of:
– int x = 10;
– cout << x;
You'll use “printf”
– printf(“hello”);
– printf(“%d”, x);
printf takes in as the first parameter a string to print out that is populated with format codes that correspond to the remaining arguments.

## Slide 23: Fwrapv, ftrapv Flags
fwrapv - instructs the compiler to assume that signed arithmetic overflow of addition, subtraction and multiplication wraps around using twos-complement representation.
ftrapv - generates traps for signed overflow on addition, subtraction, multiplication operations.

## Slide 24: Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires

## Slide 25: For example, can count in binary
Base 2 Number Representation
  Represent 1521310 as 111011011011012
  Represent 1.2010 as 1.0011001100110011[0011]……...2
  Represent 1.5213 X 104 as 1.11011011011012 X 213

## Slide 26: Encoding Integers
short int x = 15213;
short int y = -15213;
C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Two’s Complement
Sign
Bit

## Slide 27: Two-complement Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 28: Numeric Ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 29: Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform specific

## Slide 30: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
⇒ Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7

## Slide 31: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X
Mappings between unsigned and two’s complement numbers: Keep bit representations and reinterpret

## Slide 32: Mapping Signed ↔ Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
U2T
T2U

## Slide 33: Mapping Signed ↔ Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16

## Slide 34: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 35: Conversion Visualized
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Complement Range
Unsigned
Range
2’s Comp. → Unsigned
  Ordering Inversion
  Negative → Big Positive

## Slide 36: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;

## Slide 37: Casting Surprises
Expression Evaluation
  If there is a mix of unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32: TMIN = -2,147,483,648 , TMAX = 2,147,483,647

## Slide 38: Casting Surprises
Constant1 | Constant2 | Relation | Evaluation
0 | 0U | == | unsigned
-1 | 0 | < | signed
-1 | 0U | > | unsigned
2147483647 | -2147483647-1 | > | signed
2147483647U | 2147483647U | < | unsigned
-1 | -2 | > | signed
(unsigned)-1 | -2 | > | unsigned
2147483647 | 2147483648U | < | unsigned
2147483647 | (int) 2147483648U | > | signed

## Slide 39: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X ′ = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X ′
• • •
• • •
• • •
w
w
k

## Slide 40: Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 41: Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small numbers yields expected behavior

## Slide 42: Signed Binary: Two's Complement
How do we represent negative numbers?
The two's complement of a number is technically it's value subtracted from 2N.
In two's complement, most bits have the same contribution as in unsigned. The value of the i-th bit is 2^i (assuming i starts from 0).
However, the most significant bit of an N bit number has a value of -2^N-1 instead of 2^N-1

## Slide 43: Signed Binary: Two's Complement
● Assume we're dealing with four bit numbers.
● Consider the unsigned binary number 1010:
– 1010 = 1*2^3 + 0*2^2 + 1*2^1 + 0*2^0 = 10
● Now consider the signed binary number 1010:
– 1010 = 1*(-(2^3)) + 0*2^2 + 1*2^1 + 0*2^0 = -6

## Slide 44: How to convert between negative and positive
● The method: take the bitwise inverse and add one.
Consider 0101 (5).
1. 0101
2. Bitwise inverse of 0101 = 1010.
3. 1010 + 0001 = 1011.
4. Confirm: 1011 = (-(2^3)) + 2^1 + 2^0 = -5

## Slide 45: Signed Binary: Notes
● The value of a signed binary number depends on the number of bits there are.
– Four bit signed: 1111 = -1
– Five bit signed: 01111 = 15
● An N-bit signed binary number has 2^N possible values with a range of [-2^N-1, 2^N-1-1].
● REMEMBER THIS: The range of a twos complement signed binary number is not
symmetrical around 0.
● Henceforth all signed binary is two's complement unless otherwise specified.

## Slide 46: Binary arithmetic
● What does it mean to add bits?
● The idea is the same as in decimal. Let's try with unsigned.
0001 0001 0001 0011
+ 0010 + 0001 + 0111 + 0111
---------- -------- ---------- --------
0011 0010 1000 1010
Note that adding two or three 1 bits will produce a carry bit that must be added to the next bit over.

## Slide 47: Binary arithmetic
● How about subtraction? You can generalize the
decimal method for binary, but...
● The simplest way to do X – Y is to do X + (-Y).
● Take 0110 (6) – 0010 (2)
● This becomes 0110 (6) + 1110 (-2)
0110
+ 1110
----------
0100

## Slide 48: Unsigned overflow in C
● With signed arithmetic, we saw that a carry out bit was
completely valid, but what about unsigned?
● Say we have 4-bit numbers and we add 6 + 12.
● 6 = 0110, 12 = 1100
0110
+ 1100
--------
10010 = 18
● ...but this requires 5 bits to represent. We only have 4.

## Slide 49: Unsigned overflow in C
● Just drop bits.
● If an unsigned operation of an n-bit number requires more than n bits, the resulting number will consist only of the n least significant bits.
– Ex. In the previous example:
– 0110 + 1100 = (1) 0010, the leading one is dropped and instead of the right answer of 18, you get the incredibly wrong answer of 2
● More formally, if you have n-bits, the computation of x + y is (x + y) % 2n.
– Ex. (6 + 12) % 24 = 18 % 16 = 2

## Slide 50: Unsigned overflow in C
● This is also true of unsigned multiplication overflow:
● If we have 4 bits, 6 * 12 = 72
● In binary, 72 is 1001000.
● Truncate bits beyond 4 and the result is 1000 = 8.
● 72 % 24 = 8
● Keep in mind, this is for unsigned numbers only.
● Let's not think about signed numbers for now.

## Slide 51: Datatypes in C
● Each native datatype in C is expressed by a sequence of bits.
● Simple data types such as ints and shorts come in unsigned and signed variants where signed is the default (ie. int is actually a signed int)
● However, the number of bits used to express these numbers differs depending on whether the processor is 32 or 64-bit.
● ...but more on the processor definitions later.

## Slide 52: Datatypes in C
● char/unsigned char : 8-bits
● short/unsigned short : 16-bits
● int/unsigned (int) : 32-bits
Here's where it gets weird.
● In 32-bit machines:
– long/unsigned long : 32-bits
– long long/unsigned long long (further proof that a five year
old named these) : 64-bits
● In 64-bit machines:
– long/unsigned long : 64-bits
– long long/unsigned long long (ugh) : 64-bits

## Slide 53: Boolean Operators
● Boolean operators operate on a single bit.
● AND : &
– Result is 1 if both inputs are 1.
● OR : |
– Result is 1 if either of the inputs are 1.
● XOR : ^
– Result is 1 if one input is 1 and the other is 0
● NOT : ~
– Result is 1 if the input is 0.

## Slide 54: Bitwise Operators
● Bitwise operators perform repeated boolean operations on each bit of a number or pair of numbers.
● Bitwise invert (not the same as logical invert or '!')
– ~(1011) = 0100
● Bitwise AND/OR (not the same as logical AND/OR or &&/||)
– 1010 & 1100 = 1000
– 1010 | 1100 = 1110
● Bitwise XOR
– 1010 & 1100 = 0110

## Slide 55: Bitwise Operators
● Left shift/right shift (arithmetic vs logical)
● Left shift
– 0111 << 1 = 1110
● Right shift
– 1011 >> 1 = 0101 (logical)
– 1011 >> 1 = 1101 (arithmetic)
● Why two different right shifts?

## Slide 56: Logical Operators
● Where bitwise operators operate on each individual bit of a number, logical operators operate on the number as a whole
– II, &&, !
● To invert a bit sequence x, you would use ~x.
What happens if you use the logical invert '!'?
● !(1010) = 0
● !(0111) = 0
● !(0) = 1

## Slide 57: Logical Operators
● What happens when you use logical operators on numbers?
1011 && 1100?
● Non-zero numbers are interpreted as 1 and 0 is interpreted as... 0.
1011 && 1100 <=> 1
1011 && 0 <=> 0
1011 || 0 <=> 1

## Slide 58: Useful Tips

## Slide 59
x is a bit vector
if(x == 0)
return 0;
else
return 1;
OR
return !!x;

## Slide 60
a, b, and c are bits
if(a)
return b;
else
return c;
OR
return (a & b) | (~a & c)

## Slide 61: De-Morgan’s Law
a & b = ~(~a | ~b)
a | b = ~(~a & ~b)

## Slide 62: Multiplication by Shifting
● Consider the 4-bit unsigned number 0110.
– 0110 = 2^3 * 0 + 2^2 * 1 + 2^1 * 1 + 2^0 * 0 = 2^2 + 2^1 = 6
● 0110 << 1 = 1100
– 1100 = 2^3 * 1 + 2^2 * 1 + 2^1 * 0 + 2^0 * 0 = 2^3 + 2^2
– 2^3 + 2^2 = 2*(2^2 + 2^1) = 12
● x << n = x * 2^n

## Slide 63: Multiplication by Shifting
How can we think of multiplying two arbitrary (ie non-powers of two) numbers in binary?
0110 * 1011 (= 6 * 11 = 66)
= 0110 * (1000 + 0010 + 0001)
= 0110 * 1000 + 0110 * 0010 + 0110 * 0001
= 0110 << 3 + 0110 << 1 + 0110
= 0110000 + 01100 + 0110
= 1000010

## Slide 64: Division by shifting
By the same logic, this ought to work for division right?
Consider 4-bit unsigned:
– 1100 = 12
– 1100 >> 1 = 0110 = 6
Consider 4-bit signed:
– 1100 = -4
– 1100 >> 1 = 0110 = 6 (??)

## Slide 65: Division by shifting
● Previously, we tried logical right shifting (shift in zeros, but that didn't seem to pan out). This is where arithmetic right shifting steps in.
● Consider 4-bit signed:
– 1100 = -4
– 1100 >> 1 = 1110 = -2
● Logical shifting maintains correct values for unsigned operations while arithmetic shifting maintains correct values for signed operations.

## Slide 66: Access specific bits
Say you have the binary value 1010 and you only want to consider bits 1 and 2, that is, you want to transform 1010 into 0010.
1010
& 0110
------------
0010

## Slide 67: References
Slides modified from DJ Kim, UT Wang, Shikhar Malhotra and
http://www.cs.cmu.edu/afs/cs/academic/class/15213-f15/www/schedule.html

## Slide 68: Thank You